## Slide 1
Low-Power Operation:
ATmega328P vs. STM32F103
ATMEGA328P · STM32F103C8T6

## Slide 2
Selected STM32 Device
STM32F103C8T6
● STM32F103C8T6 (“Blue Pill”), STM32F10xxx Performance line, ARM Cortex-M3 core
● Chosen because it’s the standard STM32 counterpart to ATmega328P (Arduino) in coursework
● 8-bit AVR (simple sleep state machine) vs. 32-bit Cortex-M3 (dedicated PWR peripheral + NVIC wake-up)
● Note: newer STM32L0/L1/L4 add extra modes (Low-power Run, Shutdown) — not covered here; this report follows STM32F1’s PWR block
SECTION 01 / 11
LOW-POWER OPERATION

## Slide 3
Datasheet / Reference Manual Sources
# | Source | Publisher
1 | RM0008 Reference Manual (STM32F101/102/103/105/107), Rev. 21, 2021 | STMicroelectronics
2 | ATmega48A/PA/88A/PA/168A/PA/328/P Datasheet Complete, DS40002061A, 2018 | Microchip (Atmel)
3 | J. Yiu, Definitive Guide to ARM Cortex-M3/M4, 3rd ed., Ch. 9 | Elsevier
4 | “Definitive guide to ARM Cortex-M0/M0+: Low-power states” | Embedded.com
5 | “AVR Low Power Sleep Modes” | Microchip Developer Help
6 | “STM32 Low Power Modes: Sleep, Stop & Standby with HAL” | ControllersTech
Full URLs in References, end of file

## Slide 4
Low-Power-Mode Comparison (STM32F103)
Mode | Entry | Retained | Wake latency
Sleep | WFI/WFE, SLEEPDEEP=0 | CPU clock off only; peripherals run | Immediate
Stop | WFI/WFE, SLEEPDEEP=1, PDDS=0 | SRAM + registers retained | Fast (µs)
Standby | WFI/WFE, SLEEPDEEP=1, PDDS=1 | Only RTC/IWDG/backup regs survive | Slow (full reset)
● Standby exit only via NRST, IWDG reset, WKUP pin, or RTC alarm
● ATmega328P has 6 sleep modes instead of 3 (see Section 10)

## Slide 5
Power-Control Architecture
STM32 — two-tier
● Core level: SCB->SCR picks Sleep vs Deep Sleep, entered via WFI/WFE
● Chip level: ST’s PWR_CR decides if “Deep Sleep” = Stop or Standby
ATmega328P — single-tier / flat
● SLEEP instruction + SMCR.SM[2:0] directly gate clock domains
● PRR adds optional per-peripheral clock disable
● No separate power-domain controller — regulator behavior is fixed in hardware

## Slide 6
Important Registers
STM32F103
● PWR_CR — Stop/Standby select, regulator mode, PVD, flag clear
● PWR_CSR — status flags, WKUP pin enable
● SCB->SCR — Sleep/Deep Sleep, Sleep-on-Exit, SEVONPEND
● RCC_APB1ENR etc. — peripheral clock gating
● EXTI_IMR/EMR/RTSR/FTSR — external wake-up lines
ATmega328P
● SMCR — sleep enable + mode select
● MCUCR — BODS/BODSE (BOD disable during sleep)
● PRR — per-peripheral clock gating
● EIMSK/EICRA — INT0/INT1 config
● PCICR/PCMSK0-2 — pin-change interrupt wake-up

## Slide 7
Important Register Bits
PWR_CR
LPDS(0) low-power regulator · PDDS(1) Stop/Standby select · CWUF(2) clear wake flag · CSBF(3) clear standby flag · PVDE(4) voltage detector enable · PLS[7:5] PVD threshold · DBP(8) backup write protect
PWR_CSR
WUF(0) wake flag · SBF(1) standby flag · PVDO(2) PVD output · EWUP(8) enable WKUP pin
SCB->SCR
SLEEPONEXIT(1) · SLEEPDEEP(2) · SEVONPEND(4)
SMCR
SE(0) sleep enable · SM[3:1] mode select — 000 Idle, 001 ADC NR, 010 Power-down, 011 Power-save, 110 Standby, 111 Ext. Standby
Atmega328p
STM32

## Slide 8
WFI / WFE (Cortex-M3 only — no AVR equivalent)
● WFI — halt until any enabled interrupt or debug request
● WFE — halt until an event (interrupt, latched event, or any newly-pended interrupt if SEVONPEND=1)
● Depth (Sleep vs Deep Sleep) is set by SLEEPDEEP, not by which instruction is used
● ARM recommends DSB before WFI/WFE for portability
● ATmega328P: single SLEEP opcode; mode chosen purely by SMCR.SM[2:0] beforehand — no core/system split because AVR has no separate core-level sleep controller

## Slide 9
Interrupt and Wake-Up Mechanism
STM32F103
● Sleep → any NVIC interrupt wakes it
● Stop → only EXTI lines (pins, RTC alarm, PVD) wake it
● Standby → only WKUP pin, RTC alarm, NRST, IWDG
● PWR_CSR.WUF/SBF flags show wake cause; must clear via CWUF/CSBF before re-entering
ATmega328P
● Idle → any enabled interrupt
● Power-down → only async sources: INT0/INT1, PCINT0-23, TWI address match, Watchdog
● Power-save → same + Timer2 (async 32.768 kHz crystal)
● Standby/Ext. Standby → same sources as above, oscillator stays running → ~6-cycle wake
KEY DIFFERENCE
STM32 wake sources are largely mode-independent (EXTI/NVIC); ATmega328P wake sources shrink as sleep gets deeper, since clocks are physically gated

## Slide 10
Practical Applications
Scenario | Best fit | Why
Battery sensor node, periodic wake | ATmega328P (Power-down) | nA–µA range, simple SLEEP+watchdog pattern
IoT/wearable, fast burst processing | STM32 (Stop) | SRAM retained, no re-init needed
Long-life asset tracker | STM32 (Standby) or ATmega (Power-down) | Lowest current draw either way
Peripheral-heavy real-time system | STM32 (Sleep) | Peripherals stay live, fast wake
Educational / hobbyist project | ATmega328P | Simple model, big library base

## Slide 11
ATmega328P vs STM32 — Key Differences
Mode granularity — ATmega: 6 fixed modes. STM32: 3 modes, each configurable
Architecture — STM32 splits core sleep (WFI/WFE) from system power domain (PWR); ATmega is one flat register (SMCR)
State retention — STM32 Standby loses SRAM (reset reboot); ATmega never loses SRAM even in deepest sleep (clock-gated only) → ATmega's deepest mode behaves more like STM32 Stop than STM32 Standby

## Slide 12
Final Comparison Table
Feature | ATmega328P | STM32F103
Sleep modes | 6: Idle, ADC NR, Power-down, Power-save, Standby, Ext. Standby | 3: Sleep, Stop, Standby
Deepest low-power mode | Power-down — SRAM/regs retained | Standby — 1.8V domain off, SRAM lost
Sleep-control registers | SMCR, MCUCR, PRR | PWR_CR, PWR_CSR, SCB->SCR
Wake-up sources | INT0/INT1, PCINT0-23, TWI, Watchdog, Timer2 (async) | NVIC (Sleep); EXTI/RTC/PVD (Stop); WKUP/RTC/NRST/IWDG (Standby)
External interrupt wake-up | INT0/INT1 + 24 PCINTs, works even in Power-down | Up to 16 EXTI lines; only WKUP pin works in Standby
Timer operation during sleep | Only Timer2 (async crystal) in Power-save/Ext. Standby | All timers run in Sleep; only RTC/IWDG run in Stop
RTC operation | No dedicated RTC — emulated via Timer2 | Dedicated RTC, runs through Stop and Standby, can wake device
RAM retention | Always retained (clock-gating only) | Retained in Sleep/Stop; lost in Standby
Typical applications | Arduino projects, simple sensor nodes, education | IoT/wearables (Stop), asset trackers (Standby+RTC), real-time systems (Sleep)

## Slide 13
References
STMicroelectronics, RM0008 Reference Manual, Rev. 21, 2021 —
https://www.st.com/resource/en/reference_manual/rm0008-stm32f101xx-stm32f102xx-stm32f103xx-stm32f105xx-and-stm32f107xx-advanced-armbased-32bit-mcus-stmicroelectronics.pdf
Microchip Technology Inc., ATmega48A/PA/88A/PA/168A/PA/328/P Datasheet Complete, DS40002061A, 2018 —
https://ww1.microchip.com/downloads/en/DeviceDoc/ATmega48A-PA-88A-PA-168A-PA-328-P-DS-DS40002061A.pdf
J. Yiu, The Definitive Guide to ARM Cortex-M3 and Cortex-M4 Processors, 3rd ed., Ch. 9, Newnes/Elsevier, 2014
"The definitive guide to ARM Cortex-M0/M0+: Low-power states," Embedded.com —
https://www.embedded.com/the-definitive-guide-to-arm-cortex-m0-m0-low-power-states/
"AVR Low Power Sleep Modes," Microchip Developer Help —
https://developerhelp.microchip.com/xwiki/bin/view/products/mcu-mpu/8-bit-avr/structure/sleep/
"STM32 Low Power Modes: Sleep, Stop & Standby with HAL," ControllersTech —
https://controllerstech.com/low-power-modes-in-stm32/